Figure 1: Project Overview
# Project Overview

Figure 2: Project Overview
Development of a Master-Slave protocol for the Quadrocopter
Figure 3: ISO/OSI-Model
# Protocol Specification
## Packet Structure

Figure 4: Packet structure

## Response Messages

Figure 5: Response Message
The response message has the same message ID as the according request, but it has an additional leading error code in the payload data indicating the status of the request

## Parameter IDs (ParIDs)

Figure 6: ParID Composition
- Parameter IDs ensure a dynamic and flexible approach for the handling of sampling values and parameters that are not known in advance and may join the system at any state of operation
- The group ID and the sequence number form a unique identification
- The observable-bit and the type ID encode additional meta-data for every parameter
- Observables are read-only sampling values that are sent periodically

- Normal (none-observable) parameters can be set and read by polling
- Parameters are set and read by polling the slave, using the appropriate parameter IDs
- Up to 30 parameters can be set and read with one request/response-sequence

## Observables → Sampling (Frames)

Figure 7: Project Overview
- Observables are configured once and sampled/sent from the slave to the master at a defined rate without the need for polling the actual value over and over again
- For every observable a different sample-rate can be set (low, medium, high)

## Frames (Part 1)

Figure 8: Frames over time.
- The central point of the protocol is the framing mechanism
- This approach is used to ensure a dynamic way of sampling values from sensors and other data sources without knowing their actual constitution in advance
- Four frames are sent one after another in a cyclic manner, they are named from A to D
## Frames (Part 2)

Figure 9: Frames over time.
- After a super-period the frames will be repeated, holding the updated sampling values
- Between the frames there must be an adequate inter-frame space called gap
- The transmission of a packet with its trailing gap is called a sub-period
- The super-/sub-period is dependent from the baud-rates and user settings
## Frames (Part 3)

Figure 10: Frames over time.
There are a few constraints on those parameters:
- T_SUPER = 4 cdot T_ital"SUB"
- T_ital"SUB" = T_{GAP,i} + T_{FRAME,i} ` with ` i ` in ` "{A, B, C, D}"
T_{GAP,i} approx T_{FRAME,i} ` with ` i ` in ` "{A, B, C, D}"

## Frames (Part 4)

Figure 11: Frames over time.
- The highest possible sample-rate is TSUB (sampling a value in A, B, C and D)
- The lowest possible sample-rate is TSUPER (sampling a value in A, B, C, or D
- There is a third possible sample-rate in between (two times TSUB by sampling a value in the frames (A and C) or (B and D))
# Example and Explanation

Figure 12: Frame Example
- TSUB = 20ms (configured)	TaccX = TSUB = 20ms (high)
- TaccY = 2*TSUB = 40ms (medium)	TaccZ = 4*TSUB = 80ms (low)
- ParID(accX) = 0xD001 = 1101 0000 0000 0001(2)